## Slide 1: Frog-Eye Demonstration
Mickey McMahon

## Slide 2: Project Introduction

## Slide 3: Background & Motivation
Standard cameras
Shuttered, images are taken at a constant framerate
Each frame is an integration of data over the period of the shutter
Unable to capture objects moving appreciably faster than framerate1
Dynamic vision sensors
Independent pixels are captured when a change in pixel’s brightness is detected2
High temporal sampling, low latency allows for more accurate object tracking3
Used in a variety of embedded systems4
  Embodied robots
  Autonomous vehicles
  Drones
  Visual sensor networks

## Slide 4: Project Goal & Overview
Goal: To demonstrate the utility of and recreate a basic dynamic vision sensor
A user should be able to shine an infrared laser on a 4x4 array of pixels
Pixel data will be transmitted using two methods
  ‘Dumb’ method – all 16 pixels are read in a single ‘frame’ or ‘event’ (shutter camera)
  ‘Smart’ method – pixels will only be read when a change in light intensity is detected
The user will be able to further process data on the FPGA itself
  Path prediction
  Cluster finding

## Slide 5: Project Outline
Circuit design
Circuit implementation
Vivado block design
  High-level overview of FPGA configuration
Python API
  User interface for managing data transfer between PL and computer
Data processing
  Path prediction
  Cluster finding
  Read operations – ‘dumb’ and ‘smart’

## Slide 6: Project Outline
Circuit design
Circuit implementation
Vivado block design
  High-level overview of FPGA configuration
Python API
  User interface for managing data transfer between PL and computer
Data processing
  Path prediction
  Cluster finding
  Read operations – ‘dumb’ and ‘smart’

## Slide 7: Component Descriptions

## Slide 8: Circuit Design
FPGA Inputs
  ADC Line -> Voltage Translator
FPGA Outputs
  Clk
    ADC clock
  CS
    Chip-select, controls when the ADC reads
  MUX Select
    Controls which pixel to read from
  Reset
    Dumps ‘track-and-hold’ capacitor

## Slide 18: Vivado Block Design
High-level representation of the configuration between the ZYNQ processor/PL and the board’s external interfaces
Two important blocks
  GPIO block ‘frog’
    MUX Select and Reset Signals
  AXI Quad SPI
    Clk and CS

## Slide 19: Vivado Block Design
High-level representation of the configuration between the ZYNQ processor/PL and the board’s external interfaces
Two important blocks
  GPIO block ‘frog’
    MUX Select and Reset Signals
  AXI Quad SPI
    Clk and CS

## Slide 20: Python Overlay
Python API exposes programmability of FPGA through a wrapper that lets us interact directly with hardware IP blocks
Allows us to write data from the FPGA (control signals)
  ‘Frog’ GPIO
  AXI Quad SPI
Allows us to access read data from the FPGA memory (ADC data)

## Slide 21: Python Overlay

## Slide 22: Python Overlay

## Slide 23: Control Signal Layout

## Slide 24: Python Overlay

## Slide 25: Control Signal Simulations

## Slide 26
Timing diagram account for all circuit delays
Assumes fastest ADC clock and read operation
Timescale of the largest circuit delay (440ns) is orders of magnitude smaller than how fast control signals change (~3000Hz -> 330us), so circuit delays have negligible effect on output

## Slide 27
Timing diagram for outputs of FPGA at the PMOD ports
Uncertainty on writing select and reset signals of ~100us
Total time for 1 ‘event’ is ~6.7ms (150 events per second)

## Slide 29: Tests

## Slide 30: Control Signals
Used oscilloscope to verify control signal waveforms matched expected behavior from Python API
Used multimeter at circuit pins to verify all signals were being sent across lines effectively

## Slide 31: Circuit Implementation
Used multimeter to measure voltages across ‘pixel circuits’ with and without infrared laser to verify expected behavior

## Slide 32: Read Timing
Calculated framerate for ‘dumb’ readout method by averaging time-per-read over 200 events
Total time for 1 ‘event’ is ~6.7ms (150 events per second)

## Slide 33: Read Data
Verified that illuminating particular pixels one-by-one or over a predetermined path yields a reasonable result
Inevitable offset errors and uncertainty due to light ‘spilling over’ to other pixels, but maximum illumination is still over correct pixels

## Slide 34: Project Status
Accomplished
  Designed, implemented, and tested circuit board-FPGA interface that can accurately capture light data at a constant framerate, store light data on the board’s internal memory
Working
  Improving precision on data processing software to more accurately predict laser path
  Other offline data processing [Eric]
  Testing to see if read frequency can be improved by coding a selective read-out algorithm in the Python overlay

## Slide 35: Challenges & Recommendations
Challenges
  Debugging alignment issues
  Precise timing
  Powering the board
  Improper resets
Recommendations
  Analog implementation of faster read method
    Uses comparator circuits to only send select signal when light intensity over pixel has changed beyond certain threshold

## Slide 36: References
[1] IEEE Spectrum. https://spectrum.ieee.org/dynamic-vision-sensors-enable-high-speed-maneuvers-with-robots
[2] Tech Insights. https://www.techinsights.com/blog/image-sensor/dynamic-vision-sensors-brief-overview-image-sensor-techstream-blog
[3] Hindawi. https://www.hindawi.com/journals/complexity/2021/8973482/
[4] Key applications of the dynamic vision sensor, ResearchGate. https://www.researchgate.net/figure/Key-application-scenarios-of-the-Dynamic-Vision-Sensor-DVS_fig2_332388971